## Slide 1: Technical Advisory Committee
August 28, 2019
San Benito County Water District
Groundwater Sustainability Agency

## Slide 2: Overview of Agenda
Update on GSP schedule
Management areas
Update on sustainability criteria
Update on outreach
TAC next steps

## Slide 3: Highlights
Last TAC Meeting
  Hydrogeologic Conceptual Model (HCM)
  Groundwater Conditions
  Sections now on website
Public Workshop on June 18, 2019
Meeting and deliverable schedule updated

## Slide 4: Management Areas (MAs)
How defined?
Different water uses, water sources, geology, etc.
Why have them?
MAs may have different minimum thresholds + measurable objectives
MAs may have different monitoring, projects, management actions
MAs are defined to facilitate implementation of the GSP

## Slide 5: Four MAs based mostly on water supply sources
Local surface water from Hernandez and Paicines reservoirs in Zone 3
Imported Central Valley Project water in Zone 6 and in Santa Clara County

## Slide 6: Southern Management Area
Local access to Zone 3 surface water supply through groundwater recharge
Uplands, rangeland, farmland, and rural residential rely on wells
Limited local agencies

## Slide 7: Hollister Management Area
Access to Zone 3 and Zone 6/CVP supply and recycled water
Varied land uses: farmland, rural, urban, industrial, rangeland
City of Hollister and water districts: Valley Water, Sunnyslope, Pacheco Pass, Tres Pinos

## Slide 8: San Juan Management Area
Access to Zone 3 and Zone 6 surface water supply
Prime farmland, rangeland
City of San Juan Bautista and portions of Hollister, Aromas WD

## Slide 9: Bolsa Management Area
No direct Zone 3 or Zone 6 surface water supply
Predominantly agricultural and rural, limited local agencies
Relies solely on groundwater

## Slide 10: Confirmation of Management Area boundaries
Supports next steps:
Water budget analysis
Definition of sustainability criteria, e.g., thresholds
Identification of management actions and projects
Planning for monitoring and GSP implementation

## Slide 11: Ten-minute break
Update on GSP Schedule
Management Areas
Update on Sustainability criteria
  Groundwater levels
  Groundwater storage
  Groundwater quality
Update on outreach
Next steps

## Slide 12: Recap: Setting the stage to define sustainability criteria: groundwater levels
Water Table
Pump setting
Top of screen
Total well depth
Operable Range of Water Levels
What are potential undesirable results?
loss of yield in wells
impacts on flow to/from other areas
How do we identify undesirable results?
Historical lows?
Recent, shallow well construction?

## Slide 13: Recap options for minimum thresholds: historical low levels and/or well construction?
Chart: GW Elev (ft msl)
Chart: GW Elev (ft msl)

## Slide 14: Considerations on minimum thresholds for groundwater levels
North San Benito Basin hydrographs generally do not show long-term declining trends.
Droughts happen but the basin has fared well (so far, so good).
Well construction may be variable.
Discussion Points
Each groundwater user is responsible for a well and pump that produce sufficient water even with fluctuating water levels.
Management of groundwater storage capacity should not be constrained by the shallowest well(s).

## Slide 15
Considerations:
Undesirable results are significant and unreasonable
Need to quantify, be consistent among criteria and areally, to justify
Groundwater level decline due to drought is not sufficient (if basin is operated so that declines are offset subsequently)
Groundwater conditions throughout the basin
Measured with monitoring programs
Management actions avoid undesirable results and attain objectives
Minimum thresholds and undesirable results

## Slide 16: Minimum thresholds and undesirable results
Chart: GW Elev (ft msl)
Minimum Threshold
Annual reports will track groundwater level changes.
How frequent and when and how long can levels be below the minimum threshold before undesirable results occur?
    e.g., four consecutive measurements?
Consider this:

## Slide 17: Additional Key Wells have been identified
Long, complete, reliable record
Recently monitored
Geographically distributed
We need dedicated monitoring wells!
How many wells with levels below the threshold represent an undesirable result?
Consider this:

## Slide 18: How do we define Management Objectives?
Chart: Groundwater Elevation (ft msl)
Shallow monitoring wells may be needed in artesian areas.

## Slide 19: How do we define Management Objectives?
Chart: Groundwater Elevation (ft msl)

## Slide 20: How do we define Management Objectives?
Chart: Groundwater Elevation (ft msl)

## Slide 21: Sustainability Criteria – Groundwater Storage
Storage is a volume of available water, linked to groundwater levels
How much stored groundwater do we want for drought or shortage?
Change in groundwater storage is computed with the water budget
Inflows – outflows = change in storage
Undesirable result = insufficient storage to get through 5-year drought?
Measurable Objective = zero net storage change over long term
Consider this:

## Slide 22: Tracking groundwater storage
Stay tuned for next steps
Assess storage change for each MA
Assess water budget for historical droughts
Apply numerical model to future scenarios with climate change and CVP shortages
SBCWD tracks storage change annually
Cumulative storage change allows tracking year after year
Chart: Change in Storage (AF)
| 2006 | 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018
Annual Storage Change | 5461.8929 | -7554.8079 | 2353.9351 | 3311.9998 | -5611.2808 | 1412.0864 | 1407.4482 | -9473.4894 | -22080.1396 | -10435.2484 | -1830.6474 | 20485.7331 | 6109.3365
10 year Cumulative Storage Change | 0 | -2092.915 | 261.0201 | 3573.0199 | -2038.261 | -626.1745 | 781.2737 | -8692.2157 | -30772.3553 | -41207.6037 | -48500.144 | -20459.603 | -16704.2015

## Slide 23
GSP documents multiple constituents with focus on TDS and nitrate
Long-term data do not show long-term water quality deterioration
Groundwater quality is regulated by RWQCB and other agencies
What is the GSA role?
Support existing monitoring and management programs, e.g., Salt & Nutrient Management Plan, Irrigated Lands Program, Hollister Urban Area Water and Wastewater Master Plan
Avoid undesirable results from GSP management actions or projects
Maintain sustainability
Recap on groundwater quality
Consider this: What does sustainability look like?

## Slide 24
Update on sustainability criteria: groundwater quality
Identifying possible key wells for TDS and nitrate
Reviewing time-concentration graphs
Considering minimum thresholds and management objectives

## Slide 25
Minimum threshold = do better than historical high?
Management objective = established Basin Plan objective for TDS?
Consider sustainability criteria for TDS
Chart: San Juan MW-47
| 35521 | 36008 | 37135 | 37165 | 37257 | 37316 | 37347 | 37438 | 37530 | 37622 | 37712 | 37803 | 37834 | 37895 | 37987 | 38292 | 38473 | 38657 | 38808 | 38991 | 39173 | 39387 | 39539 | 39569 | 39753 | 39904 | 40087 | 40269 | 40452 | 40634 | 40848 | 41244 | 41426 | 41609 | 41760 | 41944 | 42125 | 42491 | 42675 | 43040 | 43252 | 43405
 | 2032 | 1774 | 1760 | 1996 | 1862 | 1548 | 1892 | 2004 | 1888 | 2194 | 1964 | 2208 | 1958 | 1772 | 1848 | 1414 | 1782 | 1536 | 1772 | 1436 | 1812 | 1215 | 1600 | 1760 | 1344 | 1328 | 1376 | 1200 | 1300
Consider this:

## Slide 26: Consider sustainability criteria for nitrate
Consider this:
Minimum threshold = do better than historical high?
Management objective = Basin Plan objective for nitrate?
DRAFT for discussion purposes only
Chart: San Juan MW-47
| 35521 | 36008 | 37135 | 37165 | 37257 | 37316 | 37347 | 37438 | 37530 | 37622 | 37712 | 37803 | 37834 | 37895 | 37987 | 38292 | 38473 | 38657 | 38808 | 38991 | 39173 | 39387 | 39539 | 39569 | 39753 | 40087 | 40269 | 40452 | 40634 | 40848 | 41244 | 41426 | 41609 | 41760 | 41944 | 42125 | 42491 | 42675 | 43040 | 43252 | 43405
 | 86 | 124 | 114 | 122 | 129 | 122 | 114 | 123 | 120 | 101 | 110 | 103 | 120 | 140 | 98 | 128 | 99 | 73 | 53 | 3.5 | 35.5 | 67 | 6.5 | 42 | 41.99 | 35.68 | 33.592 | 36.686

## Slide 27: Sustainability criteria: nitrate
Consider this:
Management objective = Basin Plan objective?
Minimum threshold = drinking water standard?
  GSA role?
  Continue monitoring/reporting
  Cooperate with state agencies
  Work with local water and wastewater agencies and with County
Chart: Hollister MW-17
| 35521 | 36008 | 37135 | 37165 | 37257 | 37316 | 37347 | 37438 | 37530 | 37622 | 37712 | 37803 | 37834 | 37895 | 37987 | 38292 | 38473 | 38657 | 38808 | 38991 | 39173 | 39387 | 39539 | 39569 | 39753 | 40087 | 40269 | 40452 | 40634 | 40848 | 41244 | 41426 | 41609 | 41760 | 41944 | 42125 | 42491 | 42675 | 43040 | 43252 | 43405
 | 6 | 3 | 2 | 3 | 3 | 2 | 4 | 3 | 3 | 3 | 2 | 2 | 2 | 3 | 4 | 5 | 2 | 5 | 8 | 7 | 8.3333 | 12.5 | 9.5 | 10.5 | 10.5 | 18.5 | 17 | 18 | 13 | 13 | 9.92 | 11.934 | 7.92 | 7.956
Basin Plan Objective

## Slide 28: Data gaps, monitoring, and management
Data gaps identified in Dec 2018 Data Memo and in draft GSP sections
Addressing sustainability criteria will:
  reveal more data needs
  indicate associated management actions:
    In-lieu recharge and managed aquifer recharge (MAR)
    Water demand management / conservation
    Management of well distribution and/or pumping
DWR Planning Grant Round 3 applications due by Nov 1 2019
Ideas for monitoring and management actions + projects are welcome!

## Slide 29: Update on Outreach
Website
  Updated website shows new North San Benito Basin
  Uploaded Introduction and Plan Area
  Uploaded HCM and GW Conditions
  School presentations
  County fair

## Slide 30: GSP Overview, Workshops, and TAC Meetings
Data Compilation / Data
Management System
Hydrogeologic Conceptual Model / Groundwater
Management Areas / Water Budgets
Plan Area / Institutional Setting
Sustainability Criteria
Management Actions / Monitoring
Plan Development
2018
2021
2019
2020
Kickoff workshop Nov 7 2018
HCM-GW Conditions
workshop #2 June 18 2019
Implementation workshop
Draft GSP workshop
Adoption hearing
Criteria workshop
Actions workshop
Water budget workshop
TBA Nov 2019

## Slide 31: Next Steps
TAC Meeting No. 6 Water Budget | October 30, 2019
SBCWD Board of Director’s Meeting | November 20, 2019
Workshop No. 2 Water Budget | TBA November 2019