## Slide 1: Technical Advisory Committee
August 26, 2020 2:00-4:00
Join Zoom Meeting
Zoom Meeting
https://zoom.us/j/92497853788?pwd=YnRVbU5MMWtvWWlRTkNQWXdmcjdRdz09
Meeting ID: 924 9785 3788 Passcode: 761145
San Benito County Water District
Groundwater Sustainability Agency
Or, dial by your location: +1 669 900 9128 US (San Jose)
Meeting ID: 924 9785 3788
Password: 761145

## Slide 2: Agenda
Roll call
Update on GSP Schedule and Progress
Setting Sustainability Criteria for:
  Land Subsidence
Depletion of Interconnected Surface Water
Next steps for GSP Section 6, “Sustainability Criteria”
Upcoming meetings

## Slide 3: GSP Overview
Data Compilation / Data
Management System
Hydrogeologic Conceptual Model / Groundwater
Management Areas / Water Budgets
Plan Area / Institutional Setting
Management Actions / Monitoring
Plan Development
2018
2019
2021
2020
Kickoff workshop Nov 14 2018
GW Conditions workshop June 18 2019
Evaluate actions workshop
Draft GSP workshop
Adoption hearing
Sustainability criteria workshop
Management options workshop
Water Budget workshop Date TBA 2020
TAC Meetings
Sustainability Criteria
Round 3 Monitoring Wells
MAR

## Slide 4: Recap: Ground surface vertical displacement from InSAR satellite
Suggests differential subsidence
Period of record is short
Changes are relatively small
Pattern is patchy
More monitoring needed for systematic analysis to identify any specific areas that might be subject to long-term subsidence

## Slide 5
Recap: UNAVCO stations track land surface changes around North San Benito

## Slide 6: Monitoring for subsidence is needed
Seasonal elastic variability
Linked to hydrologic conditions
Long term small downward trend, about 2 inches over 15 years

## Slide 7: Subsidence correlated to groundwater levels
Notes: .

## Slide 8: Minimum Threshold
  The Minimum Threshold for land subsidence
  is the rate and extent that interferes with surface land use
  Rate:
    Decline of more than 2 inches in any 5-year period
    Cumulative decline of more than 1 foot since 2015 (the SGMA start date)

## Slide 9: Minimum Threshold Context
  One foot of elevation change:
  Is the freeboard typically required in drainage ditches
  Is the elevation that structures must be above the 100-year floodplain
  Would spread water an additional 1,800 feet out from the shoreline of San Felipe Lake and 2,400-2,900 feet out from either side of Miller Canal and sections of the Pajaro River during a flood event

## Slide 10: Analysis of InSAR information is needed to assess extent
Extent:
InSAR mapping indicates ground surface changes 2015 to 2019 from about +0.1 feet to about -0.25 feet
Error is about +/- 0.1 feet
Annual download and screening of InSAR information
Detailed analysis for Five-Year update

## Slide 11: Measurable Objective
The Measurable Objective is to prevent subsidence.
Management Action
The management action is to maintain groundwater levels above historical lows; this should be achieved with the groundwater level Minimum Thresholds

## Slide 12: Interconnected Surface Water and Groundwater Dependent Ecosystems (GDEs)

## Slide 13: Where is groundwater coupled to surface water?
Hydraulically
Coupled
Decoupled
These are the textbook concepts, but how can you tell in practice?

## Slide 14
Well Water Levels are NOT the Water Table
Vertical and horizontal water-level gradients are common near streams.
DATA GAP: shallow monitoring wells in riparian areas are rare
Notes: .

## Slide 15
Surface Water Depletion Impacts
Downstream Flow and Water Rights
GDEs
Off-Channel Wetlands
Seasonal Streams and Rivers
Plants
(riparian vegetation)
Animals
(fish, amphibians)
Water Temperature
Passage Flows

## Slide 16: Downstream Water Users: PVWMA
No significant impact on PVWMA supplies because:
No plan to increase San Benito pumping
San Benito needs outflow to maintain basin salt balance
No impact of flow reduction when Pajaro River flows to the ocean.
PVWMA planning studies do not place emphasis on Pajaro River flows.

## Slide 17: Off-Channel Wetlands
This looks like a spring
These look like stock ponds and have low habitat value
Nature Conservancy NCCAG map
Many “wetlands” are not natural or not plausibly affected by pumping.

## Slide 18
Riparian Vegetation Impacts
For Stream Flow Depletion:
Stream Bed Elevation
For Riparian Vegetation:
About 20 feet

## Slide 19
Depth to Water <20 Feet in 1992 and 1998
October 1992
(end of drought)
April 1998
(end of wet period)

## Slide 20: The One Location where Tree Mortality was Found Tres Pinos Creek Photo taken April 2019 New nearby well a possible contributing factor

## Slide 21
N
Little or No Observed Correlation between Water Levels and Vegetation Health

## Slide 22
Little or No Observed Correlation between Water Levels and Vegetation Health

## Slide 23: Impacts on Animals
Focus on species of concern:
Tiger salamander
Red-legged frog
Birds
Steelhead trout--passage

## Slide 24
Effects of Pumping on Pacheco Creek Flow
Hypothetical 10% change in basin-wide pumping
Simulated flow in Pacheco Creek above San Felipe Lake

## Slide 25
Chart: San Benito River, June 1994
Steelhead Passage Opportunity: San Benito River
Flow profile for June 1994
6 cfs difference in flow, but still dry near Lucy Brown Lane

## Slide 26: Definition of Minimum Threshold
The Minimum Threshold for depletion of interconnected surface water is the amount of depletion associated with the lowest water levels during the 1987-1992 drought

## Slide 27: Definition of Minimum Threshold, continued
Undesirable results if >25% of wells within 1 mile of a riparian reach have a static spring water level lower than lowest spring water level during 1987-1992.

## Slide 28: Measurable Objective
The Measurable Objective is an amount of depletion that is less than the amount specified as the minimum threshold.

## Slide 29: Future Baseline Simulation: Is Threshold Likely to be Exceeded?
Only three of the 19 GDE compliance wells have simulated future baseline levels close to the MT:
Two where levels are fairly constant (Paicines Valley and west end of San Juan Valley)
One where future water levels similar to historical (near Casa de Fruta)

## Slide 30: Management Actions if Threshold is Exceeded
Recommended for consideration:
Conservation easements to reduce ag pumping near critical riffle along San Benito River
Decrease pumping near critical riffle along Pacheco Creek when flow recedes past minimum passage flow

## Slide 31: Actions not Recommended at this Time
Reoperate Hernandez Reservoir to increase releases in drought years
Preferentially deliver CVP water to parcels near riparian areas during droughts
Eradicate invasive vegetation
Irrigate riparian vegetation that is on the verge of dying
Groundwater recharge projects with habitat benefit in addition to water supply benefit

## Slide 32: Next Steps
Administrative Draft Section 6 will be sent to you for review and comment
We respond to comments, edit Admin Draft, prepare public Draft
Topics for Next TAC meeting
  Monitoring Network
  Projects and Management Actions

## Slide 33: Stay tuned
SBCWD Board of Director’s Meeting | August 26, 2020 5:00pm
Next TAC Meeting: Monitoring, Projects and Management Actions | September ? 2020
Public Workshop No. 3 Water Budget | TBA September 2020