## Slide 1: Update to Board of Directors: Draft Groundwater Sustainability Plan
June 30, 2021 Board Meeting
San Benito County Water District
Groundwater Sustainability Agency

## Slide 2: Overview of the GSP
Introduction
Plan Area
Hydrogeologic Conceptual Model
Groundwater Conditions
Water Balance
Sustainable Management Criteria
Monitoring Network
Projects and Management Actions
Implementation Plan
References

## Slide 3: Overview of the GSP: 10 Appendices
  A – SBCWD Notices/ Resolutions
  B – Memorandum of Understanding available upon request
  C – GSP Preparation Checklist (to be added later)
  D – Communication Plan (to be added later)
  E – Technical Memoranda (Data, Management Areas, DMS)
  F – Annual Reports
  G – Groundwater Model Update and Enhancement Report
  H – Dedicated Monitoring Well Program Technical Memorandum (to be added later)
  I – Managed Aquifer Recharge Technical Memorandum (to be added later)
  J – List of Public Meetings and Comments on the Plan

## Slide 4: Updates to the GSP document
Executive Summary
Completion of Introduction
Addition of CVP importation infrastructure Figure 2-7
Clarification of Water Quality sustainability criteria “Other Constituents” Section 6.6 (and Section 4.8)

## Slide 5: Highlights of the GSP: Hydrogeologic Setting
North San Benito Basin formed in 2019
A long, irregular but continuous basin with one principal aquifer
Four Management Areas
  Zone 6 and 3 boundaries
  Watershed divides

## Slide 6
Documented for SGMA sustainability indicators
Groundwater elevations
Groundwater storage
Land subsidence
Interconnected surface water and GDEs
Groundwater quality
No seawater intrusion.
Groundwater Conditions

## Slide 7: Groundwater levels and storage
11-5-35G1
Groundwater level declines have been reversed with CVP water
Groundwater levels / storage generally increased and stabilized

## Slide 8: Groundwater Conditions
Land subsidence
Uneven land settlement due to pumping and groundwater level decline
Not a known problem in North San Benito Basin
Indicated by satellite data to occur
Connected surface water - GDEs
Evaluated areas of connected surface water and groundwater
Identified stream reaches with riparian vegetation and potential steelhead habitat
Assessed potential impacts of pumping, drought, floods

## Slide 9: Groundwater Quality: Key constituents
Total dissolved solids TDS
Naturally high
Affected by irrigation return flows, wastewater disposal, etc.
Nitrate
Elevated due to agricultural activities, confined animal facilities, landscape fertilization, septic systems, and wastewater treatment facility discharges

## Slide 10
Developed using numerical model:
Historical and current conditions
  Pre-CVP Historical
  Historical Recovery
  Current
  Future Baseline
Future Climate Change
Future Growth
Water Balances
Cumulative change in storage, historical and current conditions

## Slide 11: Water balance findings
Baseline pumping of 90,089 AFY is sustainable into the future
Climate change scenarios
  Hollister, San Juan, Bolsa MAs have lower water levels between wet periods, but declines did not become larger over time
  In Southern MA, increased storage and water levels is indicated
Growth scenarios
  Lowered water levels in Hollister and Bolsa MAs, raised levels in San Juan MA, and little effect in Southern MA
Effects of climate change and growth would be additive: lowered water levels might reach minimum thresholds locally

## Slide 12
For each sustainability indicator, GSP defines
Undesirable Result – significant and unreasonable conditions for any of the sustainability indicators
Minimum Threshold (MT) – numeric value used to define undesirable results for each sustainability indicator.
Measurable Objective (MO) – specific, quantifiable goal to track the performance of sustainable management.
Sustainable Management

## Slide 13
Groundwater levels are sustainable
  MT is based on historical low levels or adjusted higher
  Measured at key wells
  Two consecutive occurrences in 60% of key wells would be undesirable
Groundwater storage is sustainable
  Groundwater levels MT is the proxy, protective of storage
Groundwater levels and storage
Chart: Date

## Slide 14: Subsidence and GDEs
Land subsidence
  No problems known
  Objective is to prevent subsidence
  Potential exists, so MT established
  0.2 feet/5 years (> 1 ft since 2015)
  Significant subsidence is unlikely to occur if groundwater levels stay above historical lows
Interconnected surface water-GDEs
Distribution and health of riparian vegetation shows little correlation to groundwater levels
Steelhead smolt migration might be impacted by pumping
Groundwater levels in near-stream wells from 1987-1992 drought used as proxy
Near-stream shallow monitoring wells needed (six being installed in 2021)

## Slide 15: Water Quality
Total dissolved solids
  Using data from triennial updates
  MT is defined as % wells exceeding the Basin Plan Objective of 1,200 mg/L
Nitrate
  Using data from triennial updates
  MT is defined as % wells exceeding the MCL of 45 mg/L
Considered sustainable given that beneficial uses are continuing
Legacy loading is a source of uncertainty in the short term
Implementation of management actions will make a difference in the long run

## Slide 16: Projects and Management Actions
Projects are substantial efforts that involve an increase in water supply or a reduction in demand
Actions provide a framework for groundwater management
establishing policies
filling data gaps with scientific studies or improved monitoring
providing for funding

## Slide 17: Projects improve water balance and quality
Develop Surface Water Storage
  Pacheco Reservoir Expansion Project
Expand Managed Aquifer Recharge
“Round 3” MAR project
Enhance Conjunctive Use
Enhance Conservation
Urban
Agricultural
Hollister Urban Area Water / WW Plan
  New local reservoir?
Zone 3 Operations Planning Tool
San Juan Bautista Regional Solution
North County Project

## Slide 18
Improve monitoring program and data management system (DMS)
Develop response plans
Enhance water quality improvement programs
Reduce potential impacts to GDEs (steelhead and riparian vegetation)
Provide long-term basin-wide funding mechanism
Provide administration, monitoring, and reporting
Management actions and monitoring

## Slide 19
A GSA is authorized to impose fees to fund GSP costs including monitoring and reporting
Fees can be based on acreage or volume of groundwater pumped
Groundwater Management fee based on analysis of GSP costs
Parcels categorized as follows:
Areas Benefiting from GSP
Upland Areas with Insignificant GSP Benefit
Major Municipal and Industrial Areas
Santa Clara County
Funding for basin-wide sustainable management

## Slide 20: Next Steps
  SBCWD GSA Board of Directors Meeting on Groundwater Management Fee
  Public Workshop and review period
  Round 3 MAR feasibility study completion
  Round 3 monitoring well installations
  Final GSP
  Adoption
  Implementation